## Slide 1: Managing Oil and Gas for Local Priorities: MOUs and Regulatory Options
Elizabeth Paranhos
elizabethparanhos@delonelaw.com
December 7, 2017

## Slide 2: Part I: Current Rules – CDPHE & COGCC

## Slide 3: Current CDPHE Rules
Tiered LDAR:
  NG Compressor Station Component Inspections are required annually, quarterly or monthly, depending on the amount of fugitive VOC emissions
  Well Production Facility Component Inspections
    Approved instrument monitoring method inspection frequency: one time, annually, quarterly or monthly, depending on the amount of fugitive VOC emissions and whether or not the facility has a storage tank; more frequent inspections for smaller sources in NAA
    Monthly AVO inspections for emissions greater than 0 and less than 20 tpy
  More stringent requirements in the Denver Ozone Nonattainment Area
Equipment subject to 95% or better controls or limits
  Storage tanks. System-wide ozone controls and STEM to ensure capture
  Glycol dehydrators
  Compressors
Venting limits/controls
  Pneumatic controllers-continuous bleed
    No bleed only for new where grid electricity is in use and it is feasible to use zero bleed
  Liquids unloading
  Associated gas from oil wells

## Slide 4: Current CDPHE Rules (Cont.)
Find and fix program for pneumatics in the Denver Nonattainment Area
    Natural gas-driven pneumatic controllers at well production facilities and natural gas compressor stations in the Denver Metro/North Front Range Nonattainment Area must be inspected periodically to determine whether the pneumatic controller is operating properly
Statewide HC task force and pneumatics task force
  Purpose to identify additional opportunities for HC reductions statewide
  Purpose to study pneumatic controllers, reasons for improper operation, and solutions

## Slide 5: CDPHE Rules: What should be updated
1) increased LDAR frequency, including continuous monitoring, statewide
2) find and fix for pneumatics statewide;
3) transmission segment sources;
4) pipeline maintenance
5) extend CTG requirements (e.g., control pumps, more R&R)
6) Zero bleed pneumatics
7) flowline monitoring

## Slide 6: Current COGCC Regulations
Venting restrictions for tanks and dehydrators
  All crude oil, condensate, and produced water tanks with uncontrolled actual emissions of VOC of 5 tpy or greater, located within 1,320 feet of a Building Unit, or a Designated Outside Activity Area shall use an emission control device capable of achieving 95% control efficiency of VOC
  All glycol dehydrators with uncontrolled actual emissions of VOC of 5 tpy or greater, located within 1,320 feet of a Building Unit , or a Designated Outside Activity Area shall use an emission control device capable of achieving 90% control efficiency of VOC
Pneumatics: Low- or no-bleed pneumatic devices must be used when existing pneumatic devices are replaced or repaired, and when new pneumatic devices are installed
Green completions required

## Slide 7: Updates to COGCC rules
Flowline rulemaking
  COGCC draft removes exception from pressure testing for lines with less than 15 psi; Specifies operators can use continuous or periodic pressure testing; Adds leak monitoring for crude oil transfer lines; Adds requirement to report hazardous gas leaks to COGCC and local governments
    Local governments pushing for more rigorous testing and other requirements
Update pre-production rules
  Tighten green completion rule
  Add drilling/construction requirements
Strengthen flaring and venting rules
  Prohibit venting other than in emergencies/safety
  Flaring limits

## Slide 8: Part II: Availability of Continuous Monitors (CH4 and VOCs)

## Slide 9: Technological Innovation
EDF methane detectors challenge, DOE, others have spurred innovation in this rapidly developing area
  Various types of CH4 sensors using lasers, hydrocarbon sensors that can be placed at the facility or fitted on mobile sources, are being developed and piloted
A number of state rules, EPA and BLM, allow for the use of CEMs
CARB rules require the use of continuous monitoring of upwind and downind ambient concentrations of CH4 at various locations at underground NG storage sites
  Must be equipped with alarm that is audible and visible at site and in remote control room

## Slide 10: PG&E’s Continuous Methane Monitor
In November 2016, PG&E installed a solar-powered continuous methane monitor at a natural gas storage facility in northern California that is being tested as a tool to continuously monitor for unplanned releases of methane
Continuous 24-hour monitoring offered by this technology could cut the time it takes to detect leaks from months to hours. This would lead to improved environmental performance and operational efficiency of gas infrastructure
This low-cost laser technology was developed by Acutect Inc., a San-Francisco-based startup company
Acutect technology was selected as one of 20 submissions received as part of the Methane Detectors Challenge. By working with EDF’s oil, gas and utility partners, Acutect will gain insight and data about how its solar-powered design performs under field conditions

## Slide 11: Other Methane Monitoring Programs
In August 2017, Shell announced a new technology trial at a wellsite in Alberta, Canada, where it is piloting a specially designed laser to continuously monitor emissions of methane. The device provides real-time data via mobile devices or web portals.
Norwegian producer Statoil has a similar field test ongoing in Texas
Picarro is a technology used to detect pipeline leaks and is up to a thousand times more sensitive and faster-scanning than incumbent technologies typically used on foot patrol. The Picarro Surveyor allows natural gas operators to survey for leaks at speeds previously impossible, while automatically mapping and displaying results in real time in a web browser for faster, more accurate leak detection.

## Slide 12: Other Methane Monitoring Programs (Cont.)
Sansit is a portable methane detector used in aboveground gas leak surveys, mobile gas leak surveys, below ground gas leak pinpointing, and gas leak mapping
Vanguard Methane Detector
  Used in detection of fugitive methane emissions at wellheads.
  self-powered wireless methane detector enables more pervasive identification of leaks even in remote locations, at a fraction of the overall cost compared to wired detectors.
  The WirelessHART Vanguard monitors methane emissions accurately for 5 years without battery replacement
  In a test of the unit, accurately reported the concentration of a passing methane plume which was verified by the optical imaging cameras

## Slide 13: CARB Requirements for Storage Sites
In March 2017, California Air Resources Board approved a new regulation aimed at curbing methane emissions that regularly escape from oil and gas operations
The regulations require continuous air monitoring at natural gas underground storage facilities
Must measure upwind and downwind ambient concentrations of methane at sufficient locations throughout the facility to identify methane emissions in the atmosphere
The monitoring system must the have the ability to store at least 24 months of continuous instrument data and the ability to generate hourly, daily, weekly, monthly, and annual reports
The monitoring system must have an integrated alarm system that is audible & visible continuously in the control room at the facility and in remote control centers

## Slide 14: Part III: Overview of Air Regulations in Boulder Country and in the Broomfield MOU

## Slide 15: APCA
  Legislature explicitly has authorized local regulation of air resources, including those that are more stringent than state requirements, and local regulation of sources not covered by state rules. C.R.S. § 25-7-128.
    (1) Home rule cities, cities, towns, counties, and cities and counties are hereby authorized to enact local air pollution resolutions or ordinances. Every such resolution or ordinance shall provide for hearings, judicial review, and injunctions consistent with section 25-7-118 to 25-7- 121 and shall include emission control regulations which are at least the same as, or may be more restrictive than, the emission control regulations adopted pursuant to this article;
      Except:
        Cannot be “more stringent than a corresponding state provision with respect to hazardous air pollutants; except that this paragraph (c) shall not limit local zoning powers and ordinances enacted pursuant to other authorities under state law”
        Must “contain provisions to ensure adequate reimbursement of state compliance and administrative expenses”
        If not included in SIP, caps civil penalty at $300 a day for violation.

## Slide 16: Boulder Air Regs
Operators must submit air quality plan demonstrating installation and operation shall to the maximum extent practicable avoid causing degradation to air quality
Plan must include the following, unless Board determines unnecessary
  Hydrocarbon LDAR + 2 day repair time
  Leak detection for pipelines and flowlines & annual pressure testing unless leak detection is continuous; monthly visual corrosion inspections
  Flare and combustion devices specifications, including use of auto-igniter
  24 hour notification of leaks

## Slide 17: Boulder Air regs-Site Specific Measures
Electric production equipment
Pipelines in lieu of trucks
Tankless facilities
Closed loop drilling, completion and operation of wells
Bleed and vent restrictions for pneumatics
90% control of liquids unloading
Pipeline maintenance venting controls
LDAR including continuous monitoring

## Slide 18: Boulder Air Quality Monitoring
Continuous atmospheric monitoring of ozone precursors, methane and benzene at stationary monitor
Authority to require continuous monitoring of oil and gas sites
IR inspection program
  2014-2016 conducted nearly 500 inspections
  Leaks detected at about 2/3 of sites
  Recurrent leaks found at about 1/3 of sites

## Slide 19: Broomfield Memorandum Of Understanding
In October 2017, city leaders approved an agreement with Extraction Oil & Gas Inc. that includes the following air quality provisions:
    use of electric drilling equipment and electrification during production
    Use pipelines to transport fluids to and from sites
    Tankless facilities & no glycol dehydrators
    BMPs for liquids unloading
    Reduction or elimination of emissions from maintenance activities such as pigging or blowdowns and notice re: maintenance activities
    Baseline and subsequent ambient air quality monitoring paid for by operator
    Quarterly LDAR for 1st 5 years & continuous pressure monitoring & 2 day repair timeframe
    BMPs during high ozone days
    Flowlines/pipelines
      2x yearly gas leak detection
      Annual pressure testing

## Slide 20: Questions?